## Slide 1: Presenting STANCE Presentation by Jason E. Hill
Presenting STANCE
Presentation by
Dr. Jason E. Hill
Co-investigators
Dr. Sunanda Mitra
Dr. Brian Nutter
Xiangyu Liu
Oliver Xie

## Slide 2: Presenting STANCE Presentation by Jason E. Hill
  Here we present the fMRI simulator STANCE, the Spontaneous and Task-related Activation of Neuronally Correlated Events simulator.
  We aim to develop this into a fully functioning MATLAB toolbox with command-line functions, that can be used to generate realistic synthetic fMRI data with MATLAB scripts.
  Currently, STANCE can generate data-driven synthetic neuronal activation “ground-truth”, to which motion, physiological and system noise can be added.
  Ultimately STANCE will also handle correlated time-series of activations and group studies. Applications: educational and statistical/analysis benchmarking.

## Slide 3: Presenting STANCE Presentation Outline
  Motivation
  Implementation 3D
  Implementation 4D
  Example results
  Conclusion

## Slide 4: Presenting STANCE Motivation: some BAD news…
The recent PNAS article, called “Cluster failure” from Anders Eklund, et al. calls into question fMRI activation mapping studies. They state that depending on the software package and settings, “that up to 70% of analyses produce at least one false positive.”
Neuroskeptic: “If there are lots of true positives, only a minority of positives will be false. It’s impossible to directly know the true positive rate, however.”
The STANCE simulator would allow researchers in neuroscience to have access to a synthetic ground-truth to benchmark analyses. This is a pressing need.

## Slide 5: Presenting STANCE Motivation: some GOOD news…
http://www.restingstate.com/2016/dynamic-functional-connectivity/
Dynamic analysis of resting state functional MRI data is a burgeoning field, but critical issues about the analysis methods and the interpretation of the results remain unclear. Sliding window correlation is widely used, but recent studies show that it does not provide an accurate estimate of the actual changes in correlation over the course of a scan. Nevertheless, differences in patient population and individual performance levels have been successfully detected using sliding windows, suggesting that the method retains sensitivity to relevant structure within the data. This symposium will bring together different perspectives on when sliding window approaches work and when they fail, discuss other techniques that may prove more sensitive to network dynamics, and begin to examine how the brain states identified with dynamic connectivity analysis relate to underlying changes in cognitive state.

## Slide 6: Presenting STANCE Motivation: Our goal
The complex nature of fMRI data generation and acquisition challenges the true estimation and interpretation of task-related activation maps or resting state functional connectivity networks, despite the use of various statistical data analysis methodologies.
The goal of developing the STANCE simulator is to generate “real-enough” resting-state and/or task-related 4D BOLD signals given certain experimental paradigms by using digital phantoms. System and physiological noise as well as motion are to be generated to serve as a reference for fMRI confounds.

## Slide 7: Presenting STANCE Implementation 3D: Select subject
  Select a subject – the one of the 20 available brains (10 male, 10 female) as provided by BrainWEB’s 20 normal anatomical brain phantoms.
  Each brain phantom has an anatomical T1-weighted volume and fuzzy membership volumes for 12 different tissues types.
Aubert-Broche, B., Griffin, M., Pike, G.B., Evans, A.C. & Collins, D.L. (Nov. 2006) “Twenty New Digital Brain Phantoms for Creation of Validation Image Data Bases,” IEEE Transactions on Medical Imaging 25(11) pp. 1410–1416.

## Slide 8: Presenting STANCE Implementation 3D: Register MNI152 to native
Register MNI152 brain to native space
Register
Affine transform of MNI152 to subject’s native space
MNI152 brain
Subject’s native space has a voxel size of 1mm3 with dimensions 181x217x181
T1-w data &12 fuzzy tissue membership volumes from one of 20 brain phantoms; average PD, T1 & T2* values for various tissues

## Slide 9: Presenting STANCE Implementation 3D: Create baseline volumes
Construct PD, T1 & T2* volumes
Generate functional space (fMRI scan)
Rotated by tilt angle.
Resize voxels and reslice volume with slice gap
and new dimensions.
Gray matter priors in functional space

## Slide 10: Presenting STANCE Implementation 3D: simulate first fMRI study
In this example, a model of photic stimulated activation of the visual cortex is defined by two ellipsoids with centers [7, -68, 8] and [-8, -65, 8] (MNI coordinates, as reported in the literature); both with the estimated volume 5,000 mm3 and aspect ratio 4:3:4, and and rotations about the X-axis of -30º and +30º respectively and 0.005 exponential falloff with a floor (min amplitude) of 0.2 of maximum. This is a model of the activation observed in the very first fMRI experiment published in 1991.

## Slide 11: Presenting STANCE Implementation 3D: model the activation map
Define activation regions from data/ shapes; Gaussian mask in MNI space
Transform & reslice activations to functional space; mask with gray matter

## Slide 12: Presenting STANCE Implementation 3D: model the BOLD response
Construct T2* volume with activation

## Slide 13: Presenting STANCE Implementation 3D: calculate the MRI signal
Solve EPI signal equation
Left: Pristine EPI signal; Right: difference between EPI signal and that with no activation.

## Slide 14: Presenting STANCE Implementation 3D: noisy data
Add noise, attenuation, motion, etc.
Left: with 4% of peak system noise; Middle: difference between noisy and pristine signals; Right: an attenuated signal (λ = 8.33 mm).
OUTPUT:
*.nii.gz
Compressed
NIFTI file

## Slide 15: Presenting STANCE Implementation 3D: define map from atlas
Activation maps may also be defined from atlases, such as AAL, Brodmann, Harvard-Oxford, Craddock and Brainnetome.

## Slide 16: Presenting STANCE Implementation 3D: define map from data
Data derived maps from www.neurosynth.org.

## Slide 17: Presenting STANCE Implementation 4D: experimental design & HRF
To generate 4D time-series the experimental design must be specified along with the hemodynamic response function (HRF) and model.
This is the sustained model of the hemodynamic response: the HRF convolved with the boxcar.

## Slide 18: Presenting STANCE Implementation 4D: HRF modeling & variability
There are various ways to model the HRF and the parameters can vary across subjects and their brains.
Gamma distribution:
Double Gamma:
Triple Gamma:
Triple Logit:
Balloon Model: ;
HRF height across brain. Source: Wu, G-R., and Marinazzo, D., "HRF in resting brain" bioRχiv (beta)

## Slide 19: Presenting STANCE Implementation 4D: HRF modeling continued

## Slide 20: Presenting STANCE Implementation 4D: OSO model of response
This is the transient model of the hemodynamic response: the HRF convolved with the derivative of boxcar (specifically at the onset and offset times). Onset to Offset response ratio set to 0.5.

## Slide 21
Source: Thomas T. Liu, “Noise contributions to the fMRI signal: An Overview” NeuroImage (2016).
Presenting STANCE Implementation 4D: noise in fMRI signals
Temperature
and
system

## Slide 22
Assuming uncorrelated noise sources, the noise in a preprocessed fMRI time series is
where sources can be classified as thermal (0) or physiological (p).
Signal image: simple average voxel by voxel across the time series ().
SNR of an individual image: .
Temporal SNR:
  Given by the mean voxel/ROI value divided by temporal standard deviation.
Sources: Triantafyllou et al., 2005; Friedmann & Glover 2006.
Presenting STANCE Implementation 4D: tSNR noise model

## Slide 23
The ratio of physiological to thermal noise can then be expressed by
Physiological noise = Bold like + non-Bold like components
where it is has been assumed that c1 and c2 are not B0 dependent.
Hence
If the temporal SNR is:
where V denotes the volume of a voxel.
Sources: Krueger and Glover, 2001; Triantafyllou et al., 2005.
Presenting STANCE Implementation 4D: tSNR noise model (cont.)

## Slide 24: Presenting STANCE Implementation 4D: noise sources
The system noise has a Rician distribution. Physiological noise in MRI signals comes from 6 sources:
The respiratory pulse (RP) follows the respiratory volume time-series (RVT) or the chest displacement time-series;
The cardiac pulse (CP) follows the pulse wave velocity (PWV);
The interaction between CP and RP (InterCRP);
The result of the respiratory response function (RRF) convolved with the RVT;
The result of the cardiac response function (CRF) convolved with heart rate variability (HRV);
Mayer waves due to variation in arterial blood pressure (BP).
The vertical displacement of the chest during regular respiration is then modeled for the ith cycle as

## Slide 25: Presenting STANCE Implementation 4D: respiratory motion
The modeling of physiological noise begins with modeling the chest displacement motion due to respiration.
The vertical displacement of the chest during regular respiration is then modeled for the ith cycle as
The vertical displacement of the chest during regular respiration is modeled for the ith cycle as where φ  [-0.5,+0.5] parametrizes the time/RI, relative to
the ith impulse; the amplitude Ai is proportional to the RI with average of 1.0 cm.

## Slide 26: Presenting STANCE Implementation 4D: respiratory volume, RRF
Next the respiratory volume and response are estimated.
The vertical displacement of the chest during regular respiration is then modeled for the ith cycle as

## Slide 27: Presenting STANCE Implementation 4D: Cardiac noise
The modeling of cardiac noise begins with modeling of the instantaneous heart beat rate from an Integral Pulse Frequency Modulation (IPFM) model.
The vertical displacement of the chest during regular respiration is then modeled for the ith cycle as
The instantaneous heart rate = (1 + m(t))/T
Analysis of HRV data for healthy subjects in a supine position yields a set of three almost equally weighted spectral bands at (VLF) ω1 = 0.01-0.03, (LF) ω2 = 0.09-0.11 and (HF) ω3 = 0.2-0.3 Hz.

## Slide 28: Presenting STANCE Implementation 4D: Pulse wave velocity, CRF
Next the cardiac pulse and response are estimated.
The vertical displacement of the chest during regular respiration is then modeled for the ith cycle as

## Slide 29: Presenting STANCE Implementation 4D: variability in tissue types
The vertical displacement of the chest during regular respiration is then modeled for the ith cycle as

## Slide 30: Presenting STANCE Implementation 4D: add motion
After the addition of physiological noise, but before adding system noise, motion is added to the time-series.
6 motion parameters can be estimated from real data.
Apply rigid body motion translations and rotations according to the slice timing of the fMRI scan.
Estimate spin-history effects geometrically by the amount of the slice volume that moves off resonance.
The vertical displacement of the chest during regular respiration is then modeled for the ith cycle as

## Slide 31: Presenting STANCE Implementation 4D: add motion
After the addition of physiological noise, but before adding system noise, motion is added to the time-series.
6 motion parameters can be estimated from real data.
Apply rigid body motion translations and rotations according to the slice timing of the fMRI scan.
Estimate spin-history effects geometrically by the amount of the slice volume that moves off resonance.
The vertical displacement of the chest during regular respiration is then modeled for the ith cycle as

## Slide 32: Presenting STANCE Example Results: experimental boxcars
From Chris Rorden’s educational website use alternating L/R-handed finger tapping task experimental design boxcars:
The vertical displacement of the chest during regular respiration is then modeled for the ith cycle as

## Slide 33: Presenting STANCE Example Results: 3D activation maps
From NeuroSynth.org construct peak sustained neurological activation maps for finger tasks based on observed amplitudes:
The vertical displacement of the chest during regular respiration is then modeled for the ith cycle as

## Slide 34: Presenting STANCE Example Results: simulated EPI signal
Synthetic fMRI data can now be constructed (with spatial variability of HRF proof-of principle in demo):
Noise standard deviations fit to what is observed in real data which varies with tissue type.
The vertical displacement of the chest during regular respiration is then modeled for the ith cycle as
(CSF dominated)
(GM dominated)

## Slide 35: Presenting STANCE Example Results: simulated EPI signal + noise
Add physiological noise and then all noise with system also:
The vertical displacement of the chest during regular respiration is then modeled for the ith cycle as

## Slide 36: Presenting STANCE Example Results: load motion time-series
Load the estimated time-series of the 6 motion parameters:
The vertical displacement of the chest during regular respiration is then modeled for the ith cycle as
Note: the y-displacement time-series is observed to be modulated by breathing.

## Slide 37: Presenting STANCE Example Results: more fully simulated EPI
Add motion and then all noise + motion:
The vertical displacement of the chest during regular respiration is then modeled for the ith cycle as
Note: motion is task dependent.

## Slide 38: Presenting STANCE Example Results: compare with real data
Compare representative voxel time-series:
The vertical displacement of the chest during regular respiration is then modeled for the ith cycle as

## Slide 39: Presenting STANCE Example Results: compare with real data cont.
Representative voxel time-series averaged over blocks:
The vertical displacement of the chest during regular respiration is then modeled for the ith cycle as

## Slide 40
THANK YOU.
Presenting STANCE